## Slide 1: 计算机组成原理实践
章亦葵、李幼萌
天津大学软件学院

## Slide 2: 2018实验1，2，3
Lab1:Data type and its memory location
Lab2:Arduino Nano Programming
Lab3:Modbus-RTU Data Transmit, Receive and Conversion
注意：
Arduino链接电路时，要断电后连接，否则可能烧毁计算机或Arduino电路板
注意保管好套件，不要丢失

## Slide 3: LAB hardware: Arduino Nano
A 8bit MCU Atmega328P
On board

## Slide 4: What is Arduino?
Arduino is an open-source electronics platform based on easy-to-use hardware and software.
Arduino was born at the Ivrea Interaction Design Institute as an easy tool for fast prototyping, aimed at students without a background in electronics and programming
Applications: IoT applications, wearable, 3D printing, and embedded environments
Teachers and students use it to build low cost scientific instruments, to prove chemistry and physics principles, or to get started with programming and robotics.

## Slide 5: Arduino Nano’s MCU(Micro Controller Unit)
ATMEL: Atmega328
Notes: 五大部件：
1.中央处理器，运算器（ALU）
2.控制器（Controller）
3.存储器（Memory）
4.输入设备（Input Device）
5.输出设备（Output Device）
概念：
总线（Bus）
寄存器（Register）
指令（Instruction）
程序（Program）

## Slide 6: AVR CPU Architecture(架构)
X86
AVR

## Slide 7: Data/Program Memory Map
哈佛结构: ATMEL、ARM9、ARM10、ARM11、51单片机
冯.诺依曼结构：Intel
哈佛结构是将指令存储器和数据存储器分开的一种存储器结构；而冯.诺依曼结构将指令存储器和数据存储器合在一起的存储器结构。
2048 byte SRAM
32768 byte Flash
(16384(=0x3FFF) word=16bit Flash)
Notes: CPU外部，采用的是冯诺依曼模型，而在CPU内部用的是哈佛结构。
Intel CPU 内部是哈佛结构，外部RAM是冯诺依曼结构（数据和指令分开）
The name Harvard Architecture comes from the Harvard Mark I relay-based computer. The most obvious characteristic of the Harvard Architecture is that it has physically separate signals and storage for code and data memory. It is possible to access program memory and data memory simultaneously. Typically, code (or program) memory is read-only and data memory is read-write. Therefore, it is impossible for program contents to be modified by the program itself.
The von Neumann Architecture is named after the mathematician and early computer scientist John von Neumann. von Neumann machines have shared signals and memory for code and data. Thus, the program can be easily modified by itself since it is stored in read-write memory.

## Slide 8: EEPROM(Electrically Erasable Programmable Read-Only Memory) 1024Byte=1K
Read/Write in a special way
Notes: It is organized as a separate data space, in which single bytes can be read and written

## Slide 9: I/O interface: Peripheral(计算机外围设备) Features
Two 8-bit Timer/Counters with Separate Pre-scaler and Compare Mode –
One 16-bit Timer/Counter with Separate Pre-scaler, Compare Mode, and Capture Mode
Real Time Counter with Separate Oscillator
Six PWM Channels
8-channel 10-bit ADC in TQFP and QFN/MLF package
• Temperature Measurement
6-channel 10-bit ADC in PDIP Package
• Temperature Measurement
Two Master/Slave SPI Serial Interface
One Programmable Serial USART
One Byte-oriented 2-wire Serial Interface (Philips I2C compatible)
Programmable Watchdog Timer with Separate On-chip Oscillator
One On-chip Analog Comparator
Interrupt and Wake-up on Pin Change

## Slide 10: Interrupt Vectors
Interrupt 中断
割込み（わりこみ）
Notes: 中断源
  引起中断的事件或原因
内部中断
外部中断
  可屏蔽中断
  非屏蔽中断

## Slide 11: Example Interrupt vector

## Slide 12: Instruction Set Summary 131 Powerful Instructions
Arithmetic and Logic Instructions
Branch Instructions
Bit And Bit-test Instruction
Data Transfer Instructions
MCU Control Instructions
Up to 20 MIPS Throughput at 20MHz
MIPS：Million Instruction Per Second

## Slide 13: 封装: TQFP 32pin Thin Quad Flat Pack

## Slide 14: Software Developing
Embedded Software
Assembly: ASM Compiler, Linker
C/C++: C++ Compiler, Linker
IDE: Integrated Development Environment

## Slide 15: Development Environment
Cross platform: Windows, MAC OSX, Linux
Simple, clear programming environment
Open source and extensible software
Open source and extensible hardware
https://www.arduino.cc/en/Main/Software

## Slide 16: Getting Started
Dowanload ZIP File (All OS)

## Slide 17: Create and use a portable version of the Arduino Software (IDE)
Download a compressed version of the Arduino IDE according to your OS;
Extract the archive content on the chosen unit HDD / USB memory
Open the extracted folder and in its root create a new directory called portable
launch the Arduino executable;

## Slide 18: Why Portable？
Easy to upgrade & migration: only need to move portable folder into the new version of Arduino, everything you have done is migrated to the new version
Easy development in a portable way: put Arduino IDE on USB disk you can development Arduino software on any PC or any Tablet
Old Version
New Version
upgraded Version
Notes: portable installation could be on a pendrive, allowing you to carry around your personal set of sketches, cores and libraries, to be used on any computer without affecting it with your files.

## Slide 19: First Project: Blink (Arduino Hello World)
USB cable to PC USB port
文件示例01.BasicBlink
工具开发板Arduino Nano
处理器Atmega328
端口COM?(选实际显示出来的端口号)
编译上传

## Slide 20: 首选项设定

## Slide 21: Blink Source Code源代码

## Slide 22: Blink: further study
Merit: simple
Demerit: delay() function prevent MCU from doing other tasks while it is running.
Notes: 虽然OS可以解决这样的问题，但是MCU的内存有限，需要使用更简洁的方法解决这样的问题

## Slide 23: BlinkWithoutDelay示例

## Slide 24: loop()
Exercise:
Create Flow Chart

## Slide 25: Arduino IDE Architecture
Directory Name | Usage
Drivers | Arduino board USB driver
examples | Arduino samples
hardware | AVR MCU Core source
java | Java VM for Arduino.exe
lib | Jar package for Arduino.exe
libraries | AVR peripheral libraries
portable | User MCU core/user peripheral libraries/user sketch books(*.ino)
reference | Help doc
tools | Compile tools related fiels
tools-builder | Compile tools related files
Notes: Drivers
Portable下还有Hardware和Libraries目录用于存储第三方和用户的sketchbook
Packages用于存储第三方的硬件Core

## Slide 26: Exec. Project1: Driving 4 LED lamp
Functions (reference sketch: Blink without delay)
LEDs can be controlled On/Off
LEDs can be controlled On/Off cyclically
LEDs can be controlled on change its illuminance by PWM function
Function Extension:
It can receive command serial port to call the above three functions

## Slide 27: 电子元件说明
热敏电阻NTC
B=3435K
R0=10K @25℃
电气符号：
光敏电阻cds
电气符号：

## Slide 28: 电子元件说明
LED（发光二极管）：长脚为正极（A），短脚为负极（K）

## Slide 29: 电阻
10K色环电阻（5环）：棕黑黑红 100*102=10K欧姆
470欧姆色环电阻（5环）：黄紫黑黑 470*100=470欧姆
色环读法：前三个环是数字，第四环是10的幂次，第五环是误差
棕 1 | 红 2 | 橙 3 | 黄 4 | 绿 5 | 蓝 6 | 紫 7 | 灰 8 | 白 9 | 黑 0

## Slide 31: ARDUINO NANO pin Function

## Slide 32: Port I/O 对应常用函数
pinMode(ledPin, OUTPUT);
digitalWrite(ledPin, ledState)
aigitalRead(ADCPin)
analogWrite(PWMPin, Value)
Value:0~255
Serial.begin(BPS);
Serial.read()
Serial.write(buf[],len)
Serial.print()
Serial.println()
…

## Slide 33: Schematic(电路图)
Arduino电路图绘制软件
http://fritzing.org/home/

## Slide 34: Wiring diagram

## Slide 35: Source Structure
setup(): hardware initialization, execute only once on power up
loop(): endless loop after setup() executed
int main(void) // hardware\arduino\avr\cores\Arduino\main.cpp
{ init();
initVariant();
#if defined(USBCON)
USBDevice.attach();
#endif
setup();
for (;;) {
loop();
if (serialEventRun) serialEventRun();
}
return 0;
}

## Slide 36: Some useful Arduino class and functions
Serial class: serial port communication
  Serial.Begin(9600);
  Serial.available();
  Serial.read();
  Serial.print(); Serial.println();
PWM: analogWrite(PORT, val) Port=LED’s pin number, val=0..255 for on Duty of PWM
Arduino Nano: pin marked with *pin 3, 5, 6, 9, 10, 11 have PWM function

## Slide 37: Exec. Project 2 Temperature and Light intensity Measuring
Requirements:
Measuring temperature
Detect light intensity
Send temperature & light intensity data to PC
Visualize temperature & light intensity

## Slide 38: Analog to Digital converter : ADC
Analog signal conversion is necessary：Analog to Digital converter，（AD转换器）(ADC, A/D, or A to D)
Resolution: Q =Vref/2M  1LSB=Q
Popular ADC type: successive-approximation ADC ( 逐次逼近模拟数字转换器 )
Conversion range(unipolar单极型ADC): 0~Vref
8bit ADC, Vref=5V,
   Q8= Vref/256= 0.01953125 (V)= 19.53125mV
10bit ADC, Vref=5V,
   Q10= Vref/1024= 0.0048828125 (V)= 4.8828125mV
12bit ADC, Vref=5V,
   Q12= Vref/4096= 0.001220703125 (V)= 1.220703125mV
M-bit digital
ADC
Analog
Voltage
Vin
Vref

## Slide 39: Example of AD conversion
10bit ADC
Vin = 3.14V，Vref=5V，M=10
DM = Vin/Q=Vin/(Vref/2M)=Vin*2M/Vref=3.14*1024/5=643dec

## Slide 40: Arduino Nano’s ADC
8 Channel of 10bit ADC， 0-5V conversion range
A0..A7

## Slide 41: AnalogReadSerial sample
int analogRead(pin)
Input: pin:A0..A7
Return: int (0 to 1023)

## Slide 42: Temperature Measuring
NTC电阻特性
RTH[Ω] T温度下的基准电阻
R0[Ω] T0温度下的基准电阻
B[K]:B常数
T0[K]:标准温度(25℃= 298.15 K)
T[K]:热敏电阻温度
实验使用的热敏电阻B常数=3435K，R0=10,000Ω

## Slide 43: Convert NTC resistance to Voltage
Vtemp = Vcc*R5/(R9+R5)
ADCdata= Vtemp/(Vref/1024)=Vtemp*1024/Vref
Where: Vcc=5V, R5=10000 Ω,Vref=5V
R9=R0*exp(B*(1/Tx-1/T0))
  B=3435K
  R0=10000 Ω; NTC resistance@25℃
  T0=25+273.15 (K)
  Tx Measured temperature （K）
Temperature to ADC Value table
Vtemp
ADC data
Notes: Exp. Function and ln function are too time consuming for mcu.
USE data table to convert

## Slide 44: Equation Temperature vs. ADC’s value
T = 摄氏度+273.15
T0 = 25+273.15 (K)
B=3435K, R5=10000,R0=10000
ADCx=温度传感器的ADC转换值= AnalogRead(A0)
Time Consuming and low efficiency for AVR CPU

## Slide 45: Linear Piecewise Approximation分段线性化
Chart: ADC-Temperature
 | 0 | 40 | 80
分段线性化
插值计算
输入ADC 值 Ax
输出温度值 Tx
(A1,T0)
(A0,T1)
(A0,T0)
(Ax,Tx)
(A0,Tx)
(Ax,T0)
ADC值
温度值
(A1,T1)
A1
Ax
A0
T0
T1
Tx

## Slide 46: Measure temperature by Arduino From piecewise linearized array
查表法
生成ΔTemp=20℃ 或10 ℃的插值计算表(误差尽量小于5%)
编写已知ADC值Ax查找其所处插值表的线段
使用该线段的两个端点的下X/Y坐标和Ax，计算Tx
使用Arduino的Serial.println输出温度值道PC
Adc值 | T
116 | -20
264 | 0
461 | 20
649 | 40
788 | 60
878 | 80
908 | 90
932 | 100
950 | 110
964 | 120

## Slide 47: 查表法计算的时间测量
初始化时间测试用管脚
Setup(){ …
bitSet(DDRB,5); //out put D13
bitClear(PORTB,5);
}
测量方法:在需要测量代码时间长度的前后放上一个改变某个管脚输出状态的语句：
Notes: 也可以用软件的micro函数测量，但是如果被测代码的执行时间超出micro的最长时间则测出的时间不可信

## Slide 48: 选择整数运算的编译结果：
程序Flash ：3204Bytes
全局变量RAM：192字节

## Slide 49: 查表整数运算时间：42us

## Slide 50: 分段线性化误差问题
Chart: ADC-Temperature
系列3 | -20 | 0 | 20 | 40 | 60 | 80 | 90 | 100 | 110 | 120
温度（℃）
ADC值

## Slide 51: 直接用公式计算温度
T=1/ (ln(Rth/R0)/B+1/T0)
={1/(ln((10000*1024/ADC-10000)/10000)/3435.0+1/298.15)}-273.15
其中：
R0=10000；
Rth=R5*1024/ADC-R5=(10000*1024/ADC-10000)
B=3435K
T0=273.15+25=298.15(K)
T=T(K)-273.15 (℃)

## Slide 52: 浮点计算编译结果
程序Flash:4906Byte 整数运算相比 多了4906-3204=1702bytes
全局变量RAM：202字节

## Slide 53: 直接浮点计算温度的时间是: 295us

## Slide 54: 浮点计算的代码的反汇编结果
Notes: “C:\arduino-1.8.2\hardware\tools\avr/bin/avr-objdump.exe" -h -S %1 >%1.lss

## Slide 55: 2次拟合方式计算：三次乘法48us，
#define DF_P2 (9.619e-05)
#define DF_P1 (0.02703)
#define DF_P0 (-15.93)
CalcTemp1=((x)*(x)*DF_P2+(x)*DF_P1+DF_P0) 三次乘法运算
CalcTemp2=((x)*((x)*DF_P2+DF_P1)+DF_P0) 两次乘法运算
三次乘法48us
两次乘法39.8us
Notes: 测试时不能两种计算放在一起，否则优化会使Port口的执行位置与源码的位置不一致，造成测量上的误测
查看lss源码会发现此问题
No optimization: -O0 speed optimization: -O3 size optimization: -Os balance optimization: -O2

## Slide 56
Notes: Volatile func 的作用可以取消对代码的优化，2，3次乘法的例子。如果有优化就无法测量出准确的结果

## Slide 57: 课上测量4us的错误原因:编译优化: -Os
编译时的优化改变了端口输出的位置
希望的是这样
编译优化后可能变为这样

## Slide 58: ATMEGA328P的指令执行时间
ATMEGA328P时钟频率是16MHz
AVR MCU的一条指令的最小执行时间 = 一个时钟周期= 1/16MHz
1/16,000,000= 62.5ns
编译优化的结果
使用volatile 修饰变量和函数防止编译对它的优化
或是把编译的优化选项关闭，例如用-O0 代替-Os

## Slide 59: Light Intensity Measure
Photoresistor Sensor:硫化镉（CdS）
It is a light-controlled variable resistor.
The resistance of a photoresistor decreases with increasing incident light intensity
实验用的光敏电阻型号GL5606

## Slide 60: Photoresistor
Disadvantage
unsuitable for applications requiring precise measurement of or sensitivity to light photons
A certain degree of latency between exposure to light and the subsequent decrease in resistance, usually around 10 milliseconds
The lag time when going from lit to dark environments is even greater, often as long as one second.
unsuitable for sensing rapidly flashing lights
Notes: 光敏电阻的主要参数是：
光敏电阻的实验图
（1）光电流、亮电阻。光敏电阻器在一定的外加电压下，当有光照射时，流过的电流称为光电流，外加电压与光电流之比称为亮电阻，常用“100LX”表示。
（2）暗电流、暗电阻。光敏电阻在一定的外加电压下，当没有光照射的时候，流过的电流称为暗电流。外加电压与暗电流之比称为暗电阻，常用“0LX”表示(用照度计测量光的强弱，其单位为拉克斯lx)。
（3）灵敏度。灵敏度是指光敏电阻不受光照射时的电阻值（暗电阻）与受光照射时的电阻值（亮电阻）的相对变化值。
（4）光谱响应。光谱响应又称光谱灵敏度，是指光敏电阻在不同波长的单色光照射下的灵敏度。若将不同波长下的灵敏度画成曲线，就可以得到光谱响应的曲线。
（5）光照特性。光照特性指光敏电阻输出的电信号随光照度而变化的特性。从光敏电阻的光照特性曲线可以看出，随着的光照强度的增加，光敏电阻的阻值开始迅速下降。若进一步增大光照强度，则电阻值变化减小，然后逐渐趋向平缓。在大多数情况下，该特性为非线性。
（6）伏安特性曲线。在一定照度下，加在光敏电阻两端的电压与电 流之间的关系称为伏安特性。在给定偏压下,光照度 较大，光电流也越大。在一定的光照度下，所加的电 压越大，光电流越大，而且无饱和现象。但是电压不 能无限地增大，因为任何光敏电阻都受额定功率、最 高工作电压和额定电流的限制。超过最高工作电压 和最大额定电流，可能导致光敏电阻永久性损坏。[1]
（7）温度系数。光敏电阻的光电效应受温度影响较大，部分光敏电阻在低温下的光电灵敏较高，而在高温下的灵敏度则较低。
（8）额定功率。额定功率是指光敏电阻用于某种线路中所允许消耗的功率，当温度升高时，其消耗的功率就降低。
（9）指光敏电阻器从光照跃变开始到稳定亮电流的

## Slide 61: 光强测量电路图
Vadc=Vcc*R6/(R7+R6)
R7 于光强成反比。The resistance of a photoresistor decreases with increasing incident light intensity
根据光强的变化定性判定光的强度:强、中、弱

## Slide 62: Project3: Connect PC to Arduino
USB Serial Port: Command & Data communication
Serial Parameter setting(4..7)
Control LED functions(2)
Read Temperature & Light Intensity (1)
Visualize the temperature & intensity data in Digital form and Real Time Graph(1, 3)
Data logging and reload(8,9)
LED state save and reload(2,8,9)

## Slide 63: Schematic（电路图）

## Slide 64: Wire diagram

## Slide 65: PWM output waveform
LED_WHITE 3 pin
占空比随光强度变化

## Slide 66: Serialport TX output waveform
Oscilloscope & Logic analyzer
Notes: 28字节 29.005ms

## Slide 67: Serialport Rx output waveform
打开Arduino的串口监视器
选择右下脚的下拉菜单选: 回车
输入1234 并按发送